# Peterson MIDI Resource System with a Rodgers MX-200

The MIDI Resource System will need to have DU1.78 or SP1.78 software to work with the Rodgers MX-200. This software has the capability to send MSB and LSB Bank selects with the Patch Change.

The voices that can be used are on page 28 and 29 of the Rodgers Owner’s Manual. By using the PC, MSB, and the LSB on the left hand column for each voice. ( PC = Patch Change, MSB = Most significant Bit Bank, and LSB = Lest Significant Bit Bank )

## Programming the Peterson MIDI Resource System

1. Programming Bank Selects-- Bank Select messages are programmed similar to other patches. While in the Program Mode: Use the Program Up/Down button to change the control panel display to where the program number is below 0 	(zero) but above 128. The Program number will change to a dash, the Manual Number will change to a lower case "b" (for Bank) and the Send light will go off. While on this display; first select the desired Channel using the Channel Up/Down button, then push the Send (or Receive) button to change the Bank Number (which is now displayed in the Program Number window) to the desired Bank Number 1-128. Now press and hold the Set piston and then press the desired numbered piston. (NOTE The Rodgers MX-200 needs to have the MSB bank sent first followed by the LSB then the PC in this order for each voice that is programmed. See Layering Bank Selects ) The display will  show  "Set" to verify the operation. Next, press the Program Up/Down button to exit the Bank position and then use the normal means-- a key press (for Manual), Channel selection (same as Bank) and Program selection, followed by Set, to add this patch as the next layer. Now when activating this piston the Bank Selects will be sent first followed by the program patch.

2.Layering Bank Selects-- When layering Bank Select messages on a preset MIDI piston or stop, the Bank Selects must be programmed (sent) prior to the Program (voice) Change message for the new bank. Thus, program the bank layers and then the program change. (Do not send all Bank messages first, but rather alternate Banks MSB and LSB and Patch.)  Be sure to use the same channel for all 3. Also note that when a Bank has been changed on a channel-- that channel will remain on that Bank until a new Bank is selected. Thus if you want to switch back to a program/voice on that channel that's on another Bank, you must send its Bank messages first. (Do not re-use the same channel on subsequent layers of the same preset piston/stop.)

Example

We will be programming The French Horn on the Swell Manual using MIDI Channel 9. First program the MSB Bank of 93, then program the LSB Bank of 126, Then the PC of #22. The windows on the MIDI Resource System will be as follows.

Man.               Channel          Program

b                        9                      93

b                        9                     126

1                        9                      22