# Peterson MIDI Resource SystemTM with an Allen Ensemble1

The voices in the two MIDI Banks of the Allen Ensemble1 can be accessed directly by sending a Bank select message of Bank 0 followed by a patch for the General MIDI Bank and a Bank select message of Bank 2 followed by a patch for the Pipe Organ Voices.

The Allen Ensemble1 will need to be set into the General MIDI Play Mode. This is done by pressing the ”FCTN” button, and using the UP and Down buttons to select the play mode, the “X” will change position to indicate which mode you are currently in. Move the “X” next to the line General MIDI Play Mode. Once the selection is complete press the “PRESET” button to set your choice in and return to the Preset combination screen. This procedure will need to be done every time the Allen Ensemble is turned off and on.

The Peterson MIDI Resource SystemTM Software needs to be 1.68 or newer and the bank select needs to be set for MSB. Using the dipswitch #2 (from the left on the Minimum I/O 404586). With the switch up (on) an MSB message is sent.

## Programming the Peterson MIDI Resource System for the Allen Ensemble1

Change the MIDI Resource SystemTM Bank Number

- In the program mode Change the Bank Number by scrolling the Program Number to the point between 0 and 128 (below zero, above 128) where a lower case "b" appears in the Manual window.

2.   Select the Channel on which the voice is to be played using the Channel Up or Down Buttons.

- Press the Send Button to increment or the Receive Button to decrement the Bank Number, (displayed in the Program Number window) to 0 for the General MIDI Bank or 2 for the Allen Ensemble1 Voices Bank. The Bank Select message is then set on the Piston (or pre-set stops).

4.   Use the Program Up (or Down) to exit the Bank Select.

- The piston (or pre-set stop) that includes the desired Channel of the Bank you have selected above /Program Numbers that will enable a selected voice. Refer to the Allen Ensemble1 manual for a list of the available voice (program) numbers. The Patch is then set on the same Piston (of preset stop).

Example: A piston could be set:

Man#  Ch#  Prg#

b        9       2        This is the Bank select for channel 9 Allen Ensemble1 Voices

1        9       2        Swell playing 16’ Diapason on MIDI channel  9 (Allen Ensemble1 voice #2)

NOTE: MIDI channel 10 is the Allen Ensemble1 Drum Set.

1.  Allen Ensemble is a trademark of Allen Organ Co., Macungie, Pennsylvania