Peterson MIDI Resource SystemTM with a Rodgers PR-3001

Programming piston (patch) changes in the MIDI Resource SystemTM that will operate an Rodgers PR-3001 (combination Sequencer/Sound Module) is accomplished as follows:

Configure the Rodgers PR-3001

To configure the Rodgers PR-3001 for use with the Peterson MIDI Resource SystemTM the Rodgers1 default Sequencer and Sound Module channels must be swapped. This is accomplished by first setting the switch on the PR-300 back panel for channels 11-16 = Internal.  Next, in the MIDI set-up menu, set channels 1-10 for External.

Programming the MIDI Resource SystemTM

Programming the MIDI Resource SystemTM pistons (or Pre-Set Stops) by is  accomplished in the normal fashion as described in the MIDI Resource SystemTM Operating Manual.

However, note that only channels 11-16 can be used for sound module voices. Therefore a maximum of six voices can be played simultaneously. These can be one voice per manual, or up to six voices on one manual.

Multiple voices from a single pre-set are available by using "Layered Patches", also described in the MIDI Resource SystemTM Operating Manual.

1. Rodgers and Rodgers PR-300 are trademarks of Rodgers Instrument Corp., Hillsboro, OR