APPLICATION NOTE:

Using the Viscount RD-70 MIDI Data Filer (Sequencer) with a Peterson MIDI Resource SystemTM

The Viscount RD-70 MIDI Data Filer must be reconfigured from the factory setting when it is to be used with the Peterson MIDI Resource SystemTM. These changes are easy to do and will be permanently stored in the RD-70, so the changes only need to be made once.

These changes are:

SOFT-THRU OFF

1. While holding ENTER, press SONG <.

(Current status of the function will be displayed.)

2. Change the status (to off) by pressing FF or REW.

3. Press ENTER to confirm (and save).

ACTIVE SENSING OFF (optional)

1. While holding ENTER, press SONG >.

(Current status of the function will be displayed.)

2. Change the status by pressing FF or REW.

3. Press ENTER to confirm.

Additional note:

When the RD-70 is used in a system with a sound module; pressing STOP or PAUSE in the middle of a song may cause the sound module notes to "hang on" (cipher). This is due to the type of "All Notes Off code that the RD-70 transmits when one of these controls is pressed. Some (usually older) sound modules do not respond to this message. If this occurs, pressing the ANO button on the Peterson MIDI Resource SystemTM will clear these notes.

A Peterson MIDI Resource SystemTM with version 2.XX software will translate the RD-70 ANO code and transmit individual note off messages to overcome this problem.